## Slide 1: 2021 California Groundwater Issues Virtual Conference February 9th and 10th, 2021 Association of Ground Water Agencies and American Ground Water Trust Presented by: Shivaji Deshmukh, General Manager, Inland Empire Utilities Agency Peter Kavounas, General Manager, Chino Basin Watermaster
MANAGING SALINITY IN THE CHINO GROUNDWATER BASIN
A TRUE REGIONAL PARTNERSHIP

## Slide 2: Presentation Outline
Regional Cooperation to manage salinity through Max Benefit
Regional use of recycled water enabled by Max Benefit
Adaptive regulation for long term regional salinity management

## Slide 3: Basin setting

## Slide 4: Basin setting

## Slide 5: Description of Stakeholders
Groundwater Pumpers (farmers, industry, retail water agencies)
Wastewater treatment agencies
Imported water agencies
Santa Ana Watershed Project Authority
Regional Water Quality Control Board

## Slide 6: Regional Cooperation to manage salinity through Max Benefit
By: Peter Kavounas

## Slide 7: Basin Plan Amendment From this:

## Slide 8: Basin Plan Amendment To this:

## Slide 9: TDS/N Limits From this:

## Slide 10: TDS/N Limits To this:
Chino Desalter
Wellfield

## Slide 11: “Maximum Benefit”
Combine Chino-1, Chino-2, Chino-3 management zones into Chino-North
Current ambient TDS for Chino-North was 330 mg/L
The “Maximum Benefit” TDS objective needed to be greater than 330 mg/L to create assimilative capacity
    Assimilative capacity provides the Regional Board with discretionary authority to permit discharges that exceed the objective

## Slide 12: “Maximum Benefit”
Regional commitments:
  Annual Reporting
  Ongoing monitoring and analysis
  Expansion of the Chino Desalters
  Expansion of artificial recharge facilities
  Blending of recycled water
  Wastewater improvement plan
  “Hydraulic Control” to protect downstream uses
Regional benefits:
  Higher TDS/Nitrogen limits
  Ongoing salt removal
  Fresh water supply
  Increased yield of the groundwater basin, and
  Ability to recharge recycled water without further treatment

## Slide 13: Regional use of recycled water enabled by Maximum Benefit
By: Shivaji Deshmukh

## Slide 14
  RW to El Prado Park
  RW to Whispering Lakes & El Prado Golf Course
  Installed distribution system in Chino/Chino Hills
  First Regional Pipeline
  Groundwater recharge with recycled water at Ely Basin
  Recycled Water Feasibility Study (2002)
  Chino Basin Facilities Improvements – Recharge (2004)
  Recycled Water Implementation Plan (2005)
  Developed Three Year Business Plan (2007)
  $650M in Capital Invested to Date
  95 Miles of Regional Infrastructure Installed
1976
2000
2005
2020
IEUA’s Recycled Water Program
Notes: 1970’s – IEUA began RW efforts by serving Whispering Lakes Golf Course, El Prado Golf Course* and El Prado Park in the Cities of Chino and Ontario
1990’s – Carbon canyon distribution system was constructed with individual agreements;
  IEUA’s first regional pipeline was also constructed at this time
  IEUA began to implement groundwater recharge with recycled water at Ely Basin (1999)
2000’s, the RW program has expanded delivery of high-quality RW for the region
  In order to promote the use of RW, IEUA adopted policies developed plans to develop and increase the use of the recycled water and incentive agencies to connect to the RW system
2007 – To reach milestone objectives of maximizing MWD rebates and other grants, 3-YR Business Plan was created with unanimous support from member agencies to dramatically increase RW use
2020
  Direct use is presently decreasing due to land use conversions from agricultural to residential and commercial use
  However, RW GWR has continued to increase over time. We are currently on target to reach a record high of GWR, fingers crossed for 16 TAF in 20/21.

## Slide 15
IEUA’s 4 regional water recycling plants produce approximately 50 MGD
Over 1,200 RW customer connections
Direct use for landscaping, agriculture, industrial use, etc.
Recharge in the Chino Basin
Discharge to the Santa Ana River
Groundwater Recharge Basins
Partners: SBCFCD, CBWCD, CBWM, IEUA
Recharge stormwater, imported and RW
21 recharge basins
13 basins permitted for RW recharge
Recycled Water System
Notes: 4 water recycling plants include RP-1, RP-4, RP-5, and CCWRF
RW is used for direct uses (landscape irrigation, farming); facilities built with regional collaboration
Partners: IEUA, San Bernardino County Flood Control District, Chino Basin Water Conservation District, and Chino Basin Watermaster (Watermaster)

## Slide 16: Regional Recycled Water Use
Chart: Historical Recycled Water Use
| 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
RW Direct Use | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 500 | 786 | 1834.6 | 1960.6 | 1791.5 | 1908.8 | 1205.3 | 1977.7 | 3793.6 | 2292.4 | 2075.1 | 1259.8 | 2732.6 | 3080 | 3296.6266 | 3936.7949 | 4307.8621 | 5348.4643 | 5230.3154 | 7538.9328 | 10040.2141 | 10403.8615 | 13371.9016 | 17304.25 | 16649.5134 | 20595.9578 | 21825.0868 | 24620.6701 | 22546.8368 | 19369.8155 | 19436.1084 | 21091.3998 | 16802.6896 | 17114.71
RW Groundwater Recharge | 507 | 500 | 505 | 185 | 48 | 158 | 1303 | 2981 | 2340 | 2684 | 7208 | 8028 | 8634 | 10479 | 13593 | 10840 | 13222 | 13934 | 13510.1 | 11542.3 | 13380.7
RW use began increasing in the 1990’s as the regional distribution system began to expand
2010 marked the first significant jump in recharge of recycled water
Recently experiencing a decrease in direct use, with an increase in RW recharged
FY2020/21 is forecasting record RW groundwater recharge with recent facility upgrades

## Slide 17: Groundwater Recharge Program
Regional hands-on program:
  Multi-agency and multi-year planning and cooperation
  Interagency flexibility: dry-year yield program (conjunctive use), agency transfers
  Proactive management
  Monitoring and reporting program
Recharging groundwater helps improve:
  Surface water by reducing street runoff, sediment and debris load
  Groundwater by reducing nitrates and TDS
Recharge has been increasingly successful
Chino Basin is a model for long-term success in groundwater management
Chart: Historical Groundwater Recharge by Source
| 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020
Recycled Water | 500 | 505 | 185 | 48 | 158 | 1303 | 2981 | 2340 | 2684 | 7208 | 8028 | 8634 | 10479 | 13593 | 10840 | 13222 | 13934 | 13510.1 | 11542.3 | 13380.7
Stormwater | 3162 | 1148 | 6284 | 3357 | 17648 | 12940 | 4745 | 10205 | 7512 | 14273 | 17052 | 9271 | 5271 | 4299 | 8001 | 9236 | 11575 | 4494 | 12861 | 9967
Imported | 6538 | 6493 | 6548 | 7607 | 12259 | 34567 | 32960 | 0 | 0 | 5000 | 9465 | 22560 | 0 | 795 | 0 | 0 | 13150 | 35621 | 7401 | 20154

## Slide 18: Regional Water Supplies
Regional water supplies includes both local and imported sources to meet demands
Local sources:
  Surface water
  Groundwater
  Desalinated water
  Recycled water
Imported sources:
  State Water Project

## Slide 19: Recycled Water Reuse
RW is ~15% of the local water supply
RW holds a critical role in the long-term water security of the region
Only new major source of water available to meet southern California’s growing water demands
Long-term increasing RW salinity trends
Increasing salinity trends pose a risk to the continued use of RW without advanced water purification
Chart: 
| Imported Water | Chino Basin Groundwater | Other Groundwater | Surface Water | CDA | Recycled Water
 | 49034.937 | 69144.049 | 26435.566 | 16652.199 | 14649.32 | 16277.846
IEUA Service Area Water Use Portfolio
FY 2019-20

## Slide 20: Adaptive regulation for long term regional salinity management
By: Shivaji Deshmukh

## Slide 21: Regulatory Requirements
Water, recycled water & wastewater quality management in Chino Basin is governed by:
Basin Plan
IEUA NPDES Permit
GWR Permit
2014 Title 22 Groundwater Replenishment Regulations
Regulatory challenges for recycled water:
Salinity (TDS)
1,2,3-TCP
PFAS
Microplastics
Constituents of Emerging Concerns (CECs)

## Slide 22: Long-Term Salinity Management
Over 15 years of major regional efforts:
  Chino Basin Desalters
  Self-generating water softener use ordinance
  Brine line discharge requirements
  Chemical use optimization in the WWTP
  Securing high quality supplemental water
Challenges with TDS
  Maximum Benefit requires a plan for treatment before exceeding limits
  In 2014/15, RW TDS was within 10 mg/l of the limit
  Drought, climate change, etc. further exacerbate TDS
  IEUA and CBWM initiated a salinity management study
Notes: The region has made commitments to implement regional programs to manage/reduce TDS
Maximum Benefit Plan enables use of RW
Non-Compliance with Maximum Benefit could prohibit use of RW

## Slide 23: Adaptive Regulation
IEUA and CBWM initiated modeling and analysis in coordination with the Regional Water Quality Control Board (RWQCB)
Question at hand:
  What are the impacts to groundwater quality in the Chino Basin if allowed a longer-term averaging period?
Will use the results to define an updated maximum benefit salinity management plan
Notes: Current averaging period for TDS is a 12-month running average
Evaluating 5- and 10-year running averages to account for hydrologic and climate conditions

## Slide 24: Study Objectives
  Develop updated modeling for the Chino Basin
  Define planning scenarios
  Evaluate impacts from climate change
  Use updated modeling tools to project the water quality concentrations
  Perform antidegradation analysis
  Use results to develop and finalize a regulatory compliance strategy
  Amend the Basin Plan to incorporate updated requirements
CHINO
BASIN
Notes: IEUA, CBWM, West Yost and the Regional Water Quality Control Board began this effort in 2016.

## Slide 25
Define
Define the TDS and nitrate loading
Establish
Establish an initial condition in the aquifer system
Define
Define salinity management scenarios and the criteria for evaluation
Estimate
Estimate future TDS and N impacts using a series of water quality models
Methodology to Evaluate Impacts of Salinity Management Scenarios

## Slide 26
  Work completed:
  Finalized proposed methods for modeling with RWQCB
  Constructed and integrated models
  Developed groundwater and vadose zone initial conditions
  Defined and calculated the Baseline conditions
  Prepared sensitivity analysis
  Upcoming effort:
  Finalize planning scenarios
  Produce and analyze modeling results
  Future planning for Advanced Water Purification Facility
  Continue working with the RWQCB to update permit
Study Progress
Notes: Together, CBWM, WEI and IEUA have undertaken a project to prepare groundwater basin modeling for TDS
The project will update the groundwater modeling for the Chino Basin to include future salinity projects, source water forecast, and groundwater conditions.
The effort will support obtaining approval for a Basin Plan amendment and permit modifications

## Slide 27: Hands-on Regional Salinity Management
Goals for long-term optimum basin management
Extensive stakeholder coordination
Close and consistent coordination with the RWQCB
Recycled and groundwater are essential Chino Basin water supplies
Collaboration and partnerships are key to regional success
Notes: IEUA is a steward of the region, responsible for managing water/wastewater
Coordination is key: held over 20 workshops related to salinity in recycled water since 2014
Critical to evaluate challenges and develop long-term solutions together
There’s an important nexus between compliance and water supply
Region has been hands-on in planning for and implementing salinity management programs

## Slide 28: Thank you for the opportunity to share the Chino Basin approach to salinity management
Shivaji Deshmukh, General Manager
Inland Empire Utilities Agency
www.ieua.org
Peter Kavounas, General Manager
Chino Basin Watermaster
www.cbwm.org